User Manual mkrecv

Author:	Matthias Heininger
Date:	20180418
Version:	0.2
# Introduction
This document describes the features of the mkrecv program. This covers some internals needed to understand the behavior of the program. All program options are listed. In addition, some configuration examples are presented that can be used to capture data from a MeekKAT D- or F-engine.
# Structure
The mkrecv program receives SPEAD heaps from one or many multicast groups and puts them, in a configurable order, into a PSR_DADA ring-buffer. The program is composed of the following C++ classes:
mkrecv::stream : public spead2::recv::stream
This class is a subclass of the SPEAD stream and the main purpose is overloading the heap_ready() method.
mkrecv::destination
This class handles a piece of memory. This is either a PSR_DADA ring-buffer slot or some allocated memory.
mkrecv::index_options
This class provides a convenient way of handling an indexing specification.
mkrecv::options
This class manages all program options, reads a configuration file (header) and updates the header which is transferred parallel to the data.
mkrecv::statistics
This class contains some counters (number of heaps, number of discarded heaps, and so on) used internally.
mkrecv::index_part : public index_options
This class performs run-time management of all index related issues including some index related counters.
mkrecv::allocator : public spead2::memory_allocator
This class is a subclass of a SPEAD allocator and implements the method for calculating the memory position inside a ring-buffer slot for each incoming SPEAD heap (allocate() method). Whenever a ring-buffer slot is full, it is released and a new slot is allocated.
mkrecv::receiver
This class ties all other classes together by creating one allocator and one stream for each multicast group. Stopping the mkrecv program is supported by sending a SIGINT signal to the process.
Due to the receiver class, the main of mkrecv is fairly simple:
#include "mkrecv_receiver.h"
int main(int argc, const char **argv)
{
 mkrecv::receiver recv;
 return recv.execute(argc, argv);
}
# Behavior
After starting the program, an optional configuration file is loaded and merged with the program options. The resulting values control the behavior of the program by specifying the network connection (interface, ports and multi-cast groups), the access to the PSR_DADA ring-buffer and the mapping of SPEAD heaps into memory locations.
The allocator, which manages the access to the PSR_DADA ring-buffer, is created next. If that fails, an error is reported and the program exits. It is not enough to put the SPEAD heaps into a ring-buffer slot, because it is not possible to allocate more than one slot at a time and when the last packets of the heaps in the current slot arrive, the first packets of heaps that will go into the next slot may have already arrived (there is no guarantee of ordering in the multicast stream). Therefore an additional temporary space for SPEAD heaps is created and managed. This content is copied into a regular slot as early as possible. In addition to the regular SPEAD heaps with data, SPEAD descriptor heaps describing data heaps are send via multicast groups. These SPEAD heaps are ignored and they are assigned to another memory space (trash).
Finally all streams managing network traffic are created and activated. They will automatically join their multi-cast group and start receiving heaps. Each stream will ask the allocator (only one does exist) for a memory location for a heap.
When an end signal is sent to a mkrecv process, the current ring-buffer slot is filled and released. After that, all streams are closed and the process exits.
The mapping of the SPEAD heaps to memory locations is based on the following schema:
1. A running index is build from a time-stamp item. The values are mapped to memory locations with the following formula:
   index := (value - first)/step
   index is an index inside a slot related to a time-stamp
   value is the item value of a heap (timestamp value)
   first is the time-stamp value of the first heap in the current slot, this value is updated when a slot is filled and the next slot is allocated
   step is the difference between successive time-stamps
2. Any other index is built by using the value of an item, apply a mask in order to ignore variable components/bits and use a list of values to determine an index:
   index := map(value & mask, list)
   index is an index related to an item
   value is the item value of a heap
   mask is a bit mask
   list is a list of values, the sequence number gives the index value
   count is the number of list elements
3. The final index is calculated using the following schema:
   pos := index[0] or
   pos := index[0]*count[1] + index[1] or
   pos := (index[0]*count[1] + index[1])*count[2] + index[2] or
   pos := ((index[0]*count[1] + index[1])*count[2] + index[2])*count[3] + index[3]
   index[i] the index values calculated in (1) and (2)
   count[i] the number of elements in the list of values of the i-th index
The memory layout is determined by the order in which the indices (except the first index derived from the time-stamp) are specified. The first index is the slowest, the last index is the fastest index.
In order to deal with the limitation of the PSR_DADA library that only one ring-buffer slot can be allocated at a time, an additional memory space is needed to store some heaps temporarily and copy them as early as possible into a regular slot. The allocator class implements a simple state machine which switches between a SEQUENTIAL_STATE and a PARALLEL_STATE starting with the SEQUENTIAL_STATE.
SEQUENTIAL_STATE:
The current ring-buffer slot and the temporary space are used in sequential order. This means that all heaps with a position (see pos in (3)) smaller than the capacity of a slot will go into a slot and all heaps which have a position larger than this capacity will go into the temporary space:
IF pos < slot.space THEN
destination := current slot
ELSE
pos := pos - slot.space;
destination := temporary space;
ENDIF
If the current slot is filled, it is released and a new slot is allocated. The internal state switches to PARALLEL_STATE. The test if a slot is filled does not use the number of completed heaps, because maybe mkrecv is too slow, may miss some heaps and therefore this number is not reliable. Instead a slot is released when a number of heaps is completed in the temporary memory (at least one heap per multi-cast group).
PARALLEL_STATE:
The current ring-buffer slot and the temporary space are used in parallel. This means that all heaps with a position (see pos in (3)) smaller than the capacity of the temporary space will go into that memory. All other heaps will go directly into the ring-buffer slot:
IF pos < temporary.space THEN
destination := temporary space;
ELSE
destination := current slot;
ENDIF
If the temporary space is filled (at least a number of heaps are completed in the current slot, same reason as before), the content is copied at the beginning of the current slot and the internal state switches to SEQUENTIAL_STATE.
# Program options
The behavior of the program is controlled via an optional configuration file and/or program options. Since all options have a default value, a strict order is given by:
an option overwrites a configuration file entry which overwrites the default value
The following table contains all program options, the corresponding key in the configuration file and the default value.
Option	Key	Default	Description
header			Name of a template header file which may include configuration options.
quiet			Only show total of heaps received
descriptors			Show descriptors
pyspead			Be bug-compatible with PySPEAD
joint			Treat all sources as a single stream
packet-size	PACKET_SIZE	spead2::recv::udp_reader::default_max_size	Maximum packet size to use for UDP
buffer-size	BUFFER_SIZE	spead2::recv::udp_reader::default_buffer_size	Socket buffer size
nthreads	NTHREADS	1	Number of worker threads
nheaps	NHEAPS	spead2::recv::stream::default_max_heaps	Maximum number of in-flight heaps
dada-key	DADA_KEY	dada	PSR_DADA ring buffer key
dada-mode	DADA_MODE	4	dada mode (0 = no, 1 = huge trash, 2 = dada, 3 = dada+slot, 4 = full dada)
netmap-if	NETMAP_IF		Netmap interface
ibv-if	IBV_IF		Interface address for ibverbs
ibv-vector	IBV_VECTOR	0	Interrupt vector (-1 for polled)
ibv-max-poll	IBV_MAX_POLL	spead2::recv::udp_ibv_reader::default_max_poll	Maximum number of times to poll in a row
udp-if	UDP_IF		UDP interface
port	PORT		Port number
	MCAST_SOURCES		List of multicast IPs
sync-epoch	SYNC_TIME	0.0	the ADC sync epoch
sample-clock	SAMPLE_CLOCK	1750000000.0	virtual sample clock used for calculations
nindices	NINDICES	0	Number of item pointers used as index
idx1-item	IDX1_ITEM	0	Item pointer index for the first index
idx1-step	IDX1_STEP	0x200000	The difference between successive item pointer values
idx2-item	IDX2_ITEM	0	Item pointer index for the second index
idx2-mask	IDX2_MASK	0xffffffffffff	Mask for using only a part of an item value
idx2-list	IDX2_LIST		A List of item pointer values for the second index
idx3-item	IDX3_ITEM	0	Item pointer index for the third index
idx3-mask	IDX3_MASK	0xffffffffffff	Mask for using only a part of an item value
idx3-list	IDX3_LIST		A List of item pointer values for the third index
idx4-item	IDX4_ITEM	0	Item pointer index for the fourth index
idx4-mask	IDX4_MASK	0xffffffffffff	Mask for using only a part on an item value
idx4-list	IDX4_LIST		A List of item pointer values for the fourth index
heap-size	HEAP_SIZE	0	The heap size used for checking incomming heaps

Table 1: mkrecv program options and configuration file entries

## Configuration file handling
A configuration file is specified by:
Name of the configuration file (--header)
The file follows the syntax of a PSR_DADA header. This means, each line has the following syntax:
<line> := [ <keyword> <whitespace> { <whitespace> } <value> ] [ '#' { <character> } ]
Keywords and values are simple sequences of digits and characters without any whitespace (blank or tab). The length of a line is not restricted. The total size of the configuration file including all modifications made by the program itself (it changes and/or adds some keyword/value pairs) is limited to DADA_DEFAULT_HEADER_SIZE (normally 4096 bytes). If a value is “unset”, the value given as default is used as long as no program option is used. This “unset” value is then overwritten with the final value. After determining the final values, the header is updated and sent via a ring-buffer.
The class options provides methods for loading a configuration file and access and manipulates keyword/value pairs.
If no configuration file is given, the header transferred via a ringbuffer contains only mkrecv program options.
## Network connection
The network connection is specified by:
- Size of a network packet (--packet-size or PACKET_SIZE)
- Size of a packet buffer (--buffer-size or BUFFER_SIZE)
- Port (--port or PORT)
- Multicast IPs (last options of program or MCAST_SOURCES)
- Network interface:
  - Netmap (--netmap-if or NETMAP_IF)
  - Plain UDP (--udp-if or UDP_IF)
  - Infiniband (--ibv-if or IBV_IF and --ibv-vector or IBV_VECTOR and --ibv-max-poll or IBV_MAX_POLL)
- Flag if all multicast groups should be handled with only one stream (--joint)
It is possible to specify multicast IP and port together as a <ip>:<port> string. This can be used in the configuration file and as program options. Several multicast addresses in the configuration file must be separated with a comma.
It is strongly recommended to use the Infiniband interface (--ibv-if) together with polling (--ibv-vector -1 and --ibv-max-poll 10).
## PSR_DADA ringbuffer
The PSR_DADA ringbuffer is specified by:
- The name of a PSR_DADA ringbuffer (--dada-key or DADA_KEY)
- A mode describing what kind of ringbuffer interaction is used (--dada-mode)
The mkrecv program is using a PSR_DADA ringbuffer to store arbitrary SPEAD heaps. These heaps must have a specific size and from some heap items, an index is calculated. In addition, the final header (modified configuration file) is transferred via the ringbuffer.
For debugging purposes it is possible to control the use of a PSR_DADA ringbuffer via the --dada-mode option:
- --dada-mode 0	No ringbuffer is used, only a small allocated memory space is used as a replacement. Since no other management (slot allocation and release or copy of heaps from temporary into a slot) is performed, this is the fastest implementation and can be used to see if the mkrecv program is fast enough to receive all SPEAD heaps from the network.
- --dada-mode 1	Instead of a slot a huge amount of memory is used.
- --dada-mode 2	The ringbuffer is used with only one slot which is never released and replaced by another slot. SPEAD heaps are not copied from the temporary space to a slot.
- --dada-mode 3	The ringbuffer is used including allocating and releasing slots. SPEAD heaps are not copied from the temporary space to a slot.
- --dada-mode 4	Full ringbuffer support (default).
## Index calculation
For each incoming SPEAD heap a memory offset into the current ringbuffer slot, temporary memory or thrash memory is calculated using some item pointer values. The primary index calculation uses some serial number (for example timestamp) stored directly as item pointer value. It is necessary to specify the item pointer index (starting with 0) and the difference between successive item pointer values:
- --idx1-item	The item pointer index of the serial number starting with 0 after the four fixed item pointers heap ID, heap size, heap offset and payload length.
- --idx1-step	The difference between two successive serial numbers. For example the difference between two successive timestamps.
All additional indices are build using an item pointer value, masking out the relevant bits and applying a map build from a list of values:
- --idx<i>-item	The i-th item pointer index starting with 0 after the four fixed item pointers.
- --idx<i>-mask	A mask for masking out the relevant bits (no shift is applied). The default is using all bits.
- --idx<i>-list	A list of values specifying a mapping of an item pointer value to an index. The index is determined by the position of a value in the list.
The number of item used for index calculation is given by:
--nindices	The number of item pointers used for index calculation.
# Examples
The minimal configuration file for a mkrecv process receiving SPEAD heaps from an F-engine is:
# Network connection
PACKET_SIZE 1500
BUFFER_SIZE unset
NETMAP_IF unset
UDP_IF unset
IBV_IF 192.168.1.20
IBV_VECTOR -1
IBV_MAX_POLL 10
PORT 60416
MCAST_SOURCES 224.2.1.150,224.2.1.151,224.2.1.152,224.2.1.153
# PSR_DADA ringbuffer
DADA_KEY dada
DADA_MODE 4
# Timing
SYNC_TIME 1231235243.0000000
SAMPLE_CLOCK 1750000000.0
# Additional configuration
NTHREADS 32
NHEAPS 64
# MeerKat F-Engine
NINDICES 2
# The first index item is the timestamp
IDX1_ITEM 0
IDX1_STEP 0x200000
# The second index item is the frequency
IDX2_ITEM 2
IDX2_MASK 0xffffffffffff
IDX2_LIST 0,256,512,768
The minimal configuration file for a mkrecv process receiving SPEAD heaps from a packetizer is:
# Network connection
PACKET_SIZE 5400
BUFFER_SIZE unset
NETMAP_IF unset
UDP_IF unset
IBV_IF 192.168.1.20
IBV_VECTOR -1
IBV_MAX_POLL 10
PORT 7148
MCAST_SOURCES 225.0.0.152,225.0.0.154
# PRS_DADA ringbuffer
DADA_KEY dada
DADA_MODE 4
# Timing
SYNC_TIME 1231235243.0000000
SAMPLE_CLOCK 1750000000.0
# Additional configuration
NTHREADS 32
NHEAPS 64
# MeerKat Packetizer
NINDICES 1
# The first index item is the running timestamp
IDX1_ITEM 0
IDX1_STEP 4096
This configuration file receives the SPEAD heaps for one polarization only. If both polarizations are wanted, a change is necessary to ensure that all SPEAD heaps have an unique heap id.